## Slide 2: pLED 2014
Ha Noi, April 26th

## Slide 3: Introduction Team
1
2
Nguyễn Thanh Tùng : PM, Designer, Tester
Nguyễn Thế Long: Technical Leader, Developer
Đỗ Văn Ban: Mechanic, Tester
Đinh Xuân Bách: QA, Test Leader
Đinh Quang Hải: Developer, Designer
pLED Team

## Slide 4: Contents
1
2
1
2
4
5
3
6
7
8
Introduction
Management Plan
Requirement
Specifications
Design
Implementation
Testing and Quality Assurance
Demo
Conclusion and Q&A

## Slide 5: Introduction
Persistent of Vision : The phenomenon of the eye by which an after-image is thought to persist for approximately one twenty-fifth of a second on the retina, create a illusion of existing object when there was none.

## Slide 6: Introduction
Idea Base on Persistence of Vision phenomenon, we have made a device that can create a clock, a picture, a animation screen in front of audiences.

## Slide 7: Introduction
Scope
System will:
Display 4 modes
Remote control using radio frequency
Display Real – Time Clock (GMT + 7)
Store data and require one-time setup only

## Slide 8: Introduction
Existed product : “Bob Blick‘s propeller clock”

## Slide 9: Introduction
Existed product : “AVClock”

## Slide 10: Management Plan
Software Process Model: Iterative and Increment Development (IID)

## Slide 11: Management Plan
Delivery : 17/4/2014
Efforts : 5 mem/month
Duration : 3 months
Budget: 92 million VND 

## Slide 12: Management Plan
Risk Management
No experiences design hardware
Uncontrollable outsourcing
Limited physical components
Less experiences estimate time and resource

## Slide 13: Management Plan
Role and Responsibilities

## Slide 14: Management Plan
Configuration Management
Using google code : https://pled.googlecode.com/svn/
Document and file must be save on right folder SVN
Version of document must be increase if it was changed
When commit file and document into SVN member must be write comment or message

## Slide 15: Requirement Specifications
User Requirements
User
Real – Time Clock
Decorating
Student
System demo when learn Embedded System

## Slide 16: Requirement Specifications
System Specification
Using Microcontroller
Multicolor image, clock
Remote control
One-time setup
Real-time clock built-in
Electrical standard (220v AC)

## Slide 17: Requirement Specifications
Functional
Display digital clock
Display analog clock
Display image
Display text
Setup time

## Slide 18: Requirement Specifications
Non - Functional
System stable
Picture display smoothly
Usability
Safety

## Slide 19: Requirement Specifications
Infrastructure and Tools
Hardware
PIC16F887
DS1307
EEPROM
LED RGB
Radio Frequency Module
Shift Register
IC 7805
Motor

## Slide 20: Requirement Specifications
Infrastructure and Tools
Software
ISIS Proteus
Altium Designer 10
IDE CCS C 5.015
Pickit 2 programmer
Visual Studio 2012 and .NET 4.0
Electronic multi-meter

## Slide 21: Design
Architecture Design
Block Diagram

## Slide 22: Design
Mechanical
Include: rotation + supply power

## Slide 23: DC MOTOR
Rotation
Speed: 1800rpm(1200-2000rpm)
Supply power: 5V-2A

## Slide 24: Design
Mechanical
VCC
Motor
Bearing
VCC
Shaft
Plastic
GND

## Slide 25: Design
Schematic, PCB Design

## Slide 26: Design
Printed Circuit Design

## Slide 27: Design
Architecture Design
Use case

## Slide 28: Design
Display Mode
  MODE_A: Analog Clock
  MODE_B: Digital Clock
  MODE_C: Still image
  MODE_D: Running text

## Slide 29: Design
Screen 16 LEDs x 60 NODEs

## Slide 31: Implementation
Mechanical
Motor
Rolling-element bearing
Nut and bolt
Spring

## Slide 32: Implementation
Mechanical

## Slide 33: Implementation
Circuit Board
pLed dual and triple color v1.0 (legacy)

## Slide 34: Implementation
Circuit Board
pLed triple color v2.0

## Slide 35: Implementation
LED’s data structure INT16[3]
 | BYTE 1 |  |  |  |  |  |  |  | BYTE 0 |  |  |  |  |  |  | 
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | LED1 | LED2 | LED3 | LED4 | LED5 | LED6 | LED7 | LED8 | LED9 | LED10 | LED11 | LED12 | LED13 | LED14 | LED15 | LED16
rgb_bits.blue |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
rgb_bits.red |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
rgb_bits.green |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 36: Implementation
Timing algorithm
The system use 2 interrupts to acknowledge when a new rotation started and when to print out the next Position’s data of LEDs array.
Each Hall interruption indicates when the array LED has finished a rotation.

## Slide 37: Implementation
System structure

## Slide 38: Implementation
Fetch_data()  rgb_bits
  Mode
  Node Position
  Time
  Image data
  State variables

## Slide 39: Implementation
Analog Clock

## Slide 40: Clock Mode

## Slide 41: Implementation
Digital Clock

## Slide 42: Implementation
Image

## Slide 43: Implementation
Text

## Slide 44: Image & Text Mode

## Slide 45: Implementation
Modify Driver: performance
Before optimization
40 state changes take 7/10 rotation
After Optimization
40 state changes take 3/10 rotation

## Slide 46: Implementation
Setup Time

## Slide 47: Testing &QA
Defect Log

## Slide 48: Testing &QA
Test Report

## Slide 49: Testing &QA
Quality Assurance
4 bugs after release
4 bugs into 1 issue

## Slide 50: Lesson learnt
Obstacles
Solution
Limited hardware option
Processing power is a lot lower than expected
Soldering quality is low
Inexperienced in estimate time schedule
Re-inspect the market and buy extra amount if possible
Optimize driver and using multiple backup algorithms
Manually checking circuit board’s completion and self-learn soldering
Asking for supervisor suggestion

## Slide 51: Suggested improvement
Using higher performance controller, 16bits chip is recommended
Develop team’s own soldering staff for easier maintain and customization
Use popular components for easier acquire, replacing ,and better community’s support.
Frequently asking for professional opinion to avoid rookie mistakes.

## Slide 52
Thank You !

## Slide 53
Question and Answer